RasPi Connector Pinout

Pin	Name	To/From Pi	owner	Use
1	3.3V	From		-
2	5V	From		-
3	GPIO2 / SDA1	BiDir	Both	I2C SDA
4	5V	From		-
5	GPIO3 / SCL1	From	Both	I2C SCL
6	GND	From		-
7	GPIO4	To	RG	isGun1On – signals that the Gun1 trigger is pulled
8	GPIO14, TXD
9	GND	From		-
10	GPIO15, RXD	To
11	GPIO17	?	RG	gfx doMove;
12	GPIO18	From	RG	enZ1 – Scope 1 Intensity
13	GPIO27	To	RG	isButton – application interrupt signal
14	GND	From		-
15	GPIO22	From	RG	gfx doDraw
16	GPIO23	From	RG	enZ2 – Scope 2 Intensity
17	3.3V	From		-
18	GPIO24	To	RG	isGun2Pulse – single pulse per trigger pull
19	GPIO10 / SPI-MOSI	From	RG	SPI MOSI
20	GND	From		-
21	GPIO9 / SPI-MISO	To	RG	SPI-MISO
22	GPIO25	To	RG	isGun1Pulse – single pulse per trigger pull
23	GPIO11 SPI-SCLK	From	RG	SPI-CLK
24	GPIO8 / SPI_CE0	From	RG	SPI Select for DAC
25	GND	To		-
26	GPIO7 / SPI-CE1	To	RG	isGun2On – signals that the Gun2 trigger is pulled
27	ID_SD			-
28	ID_SC			-
29	GPIO5	BiDir	RG	GPIO05 – toggle switch
30	GND	From		-
31	GPIO6	BiDir	RG	GPIO06 – toggle switch
32	GPIO12
33	GPIO13		GF	Power control output
34	GND	From		-
35	GPIO19	To	GF	Rotary Encoder phase1
36	GPIO16	To	GF	Rotary Encoder phase2
37	GPIO26	To	GF	Rotary Encoder push button
38	GPIO20	BiDir	RG	GPIO20 – toggle switch
39	GND	From		-
40	GPIO21	BiDir	RG	GPIO21 – toggle switch

Address Map

Lights / IS31FL Drivers

I2C	Row Addr aka Frame	Bits	Ref Des	Function
74	0	7:0		MAR
		15:8

Power shutdown button
https://forums.raspberrypi.com/viewtopic.php?t=371129

dtoverlay=gpio-shutdown,gpio_pin=15
gpio=23=op,dh

RetArsonFD
Posts: 9
Joined: Sun Jan 03, 2021 3:49 pm
### Re: How to do a soft shutdown on headless Pi?
Mon Mar 08, 2021 12:58 pm
RonR wrote: ↑
Mon Mar 08, 2021 4:46 am
Another option is to connect a Normally Open (NO) Single Pole Single Throw (SPST) momentary pushbutton switch to GPIO header pins 5 and 6 on the Raspberry Pi and add the following line to /boot/config.txt:
Code: Select all
dtoverlay=gpio-shutdown

Pressing the button on a running system will initiate a graceful shutdown (shutdown -h now). Watch for the green LED to blink 10 times and it's safe to turn off the power. If you don't turn off the power, pressing the button again will restart the system.

B.Goode
Posts: 17352
Joined: Mon Sep 01, 2014 4:03 pm
Location: UK
### Re: How to do a soft shutdown on headless Pi?
Mon Mar 08, 2021 1:26 pm
RetArsonFD wrote: ↑
Mon Mar 08, 2021 12:58 pm
Where would I put the "dtoverlay=gpio-shutdown" command ? If I remember what I've been told, there are numbered lines in the config txt ??

No. The format of the config.txt file is documented here. It is not numbered. https://www.raspberrypi.org/documentati ... /README.md
The specific details of the dtoverlay=gpio-shutdown configuration option are here - https://raw.githubusercontent.com/raspb ... ays/README